## Slide 1: Mouse Minder
Conrad Farnsworth

## Slide 2: Requirements
Activate when a trap trips
Audible for 1 week
Replaceable battery
Clips on to any spring driven mouse trap
Resettable
Testable

## Slide 3: First Prototype

## Slide 4: Prototype Notes
That just worked. My circuits never just work.
Things I want in V2
  A louder buzzer (optional)
    Looking at charge pumps/voltage doublers
  Buzzer as a sensor
    Bypass/isolate for just buzzer
    Separate input for another sensor
    1M pot for testing
  Test button
    I already had that but I want it as a button next
  Battery holder
    And pads for ext power
  Buttons should be hard plastic so you can use a paper clip for reset/test
  Mounting holes/extra clearance for mounting into a 3D print

## Slide 5: Plan
Buzzer as a sensor
  Do not use the charge pump on this version, too many complications
  Data looks good!

## Slide 6: Schematic
Buzzer/Sensor
Micro
Sensing CKT
Push-Pull Driver
Isolation*
*Preserves signal from the buzzer as a sensor. May not be required
Coin Cell
We could put a charge pump between the micro and driver but I am scared about increasing complexity.

## Slide 7: Second Prototype
Very promising 4/5 detections.
Piezo as sensor. Extra mosfet to drive the piezo buzzer.

## Slide 8: Third Prototype Plan
In progress as of writing this.
Pared down a lot of the schematic.
Sent to JLC for QTY5 fab. Probably should have waited. Oh well.
Need to test a few things:
  100k pull-down on ngate
    With & without R7
  330k pull-down on ngate
    With & without R7
  Tap Test
  Mosfet bypass (attiny) buzzer
    Is R7 necessary here?
    Is D4 necessary?
  Can R4 be bypassed?

## Slide 9: 1) Electrical Tests On 2nd Prototype
100k R8, RV1 Removed, R7=1k
  Measure PZ+ and NGATE
  Tap Test

## Slide 10: 1) Electrical Tests On 2nd Prototype
100k R8, RV1 Removed, R7=1k
  Measure PZ+ and NGATE
  Trap Test

## Slide 11: 2) Electrical Tests On 2nd Prototype
100k R8, RV1 Removed, R7=DNP
  Measure PZ+, NGATE, and sound.
  No Sound with DNP and me pressing test button.

## Slide 12: 3) Electrical Tests On 2nd Prototype
100k R8, RV1 Removed, R7=DNP, Bodge ATTINY pin 4 onto PZ+
  Measure PZ+, NGATE, and sound.
Sound is good, can’t turn it off (idles high)
Tap test and mouse trap test won’t trigger
  Piezo is going through protection diodes
Sensor is less sensitive than with R7 installed 
What if we make R7 Bigger?...

## Slide 13: 4) Electrical Tests On 2nd Prototype
100k R8, RV1 Removed, R7=10k, Bodge ATTINY pin 4 onto PZ+
  Measure PZ+, NGATE, and sound.
Buzzer is 15nf±30% (10.5n-19.5n)
  Want 5Tau of bleed at 4khz = 1.2k. Shit.
It’ll just be quieter. Not super interested in that.

## Slide 14: 5) Electrical Tests On 2nd Prototype
100k R8, RV1 Removed, R7=DNP
  Measure PZ+ and NGATE
  Trap Test. Won’t be able to hear anything but Let’s see how much signal that R7 was stealing away….

## Slide 15: 5) Electrical Tests On 2nd Prototype
Oh wow. 2 big learnings from that one:
  Piezo is backwards.
  R7 is stealing a LOT of signal.
  Notice PZ+ Had to be changed to 10V/div.
  Couldn’t get a trig on mouse trap. Will try again with reversed piezo

## Slide 16: 6) Electrical Tests On 2nd Prototype
Piezo flipped around.
  Measure PZ+ and NGATE
Piezo doesn’t seem to have a polarity
Piezo is also collapsing to zero…it should have 3V on it at all times….

## Slide 17: 7) Let’s put R7 Back
R7=1k
Signal Comes back

## Slide 18: 7) Let’s put R7 Back
R7=10k
Much quieter but much more sensitive.
I think a large R7 is necessary for good sensitivity. I also think we should move Q2A (Nmos) down in parallel to give max sound.
This trigger was a light tap by the way.

## Slide 19: What do I do?
REV3 is in PROD right now.
It’ll WORK but I NEED(?) to test the H-bridge before I can send it out to fab.
I should make a 3.5 change and ask JLC to prod
  Can’t cancel after it’s in prod
Use the LPKF to proto this one out?
  N/P, some resistors, header, buzzer should be a super small board…
Keep Rev2 as-is and take mouse measurements

## Slide 20: Fake Mouse Measurement
R7 = 10k

## Slide 21: Real Mouse Measurement

## Slide 22: Real Mouse Measurement PT2

## Slide 23: I had a thought…
R7 was a huge lever arm but really, C1 is the ticket.
The piezo is like 10nF and the C1 is 100n. Let’s move R7 back to 1k and change C1 to 10n.
I’m such a goof. You can see it plain as day in the DNP R7 plots. Really high negative voltage (D1 not in conduction). Really low forward voltage (capacitive voltage divider with D1 in conduction).
Way more sensitive. And I don’t need an extra mosfet….See next slide for data.

## Slide 24: R7 = 1k, C1=10n, Gentle Tap Test

## Slide 25: R7 = 1k, C1=10n, Trap Test

## Slide 26: Conclusive enough for me…
Skip the extra mosfet pair.
Power the speaker through the diode with the ATTINY
Use 1k Pull-down on piezo
Use 10nF sensitive capacitor in with 100k R8

## Slide 27: AS-BUILT (JLC QTY 5)

## Slide 28: CHANGES TO MAKE

## Slide 29: Changes Made

## Slide 30: Low Power Testing
20nA draw when not triggered (1000 year battery life lmao)
~1.05mA average when triggered. Need to get this down
  8.7 days of chirping.
LED resistor was modified for 6mA of draw but the device only seems to see 3mA of draw (resistor sized for min Vf)

## Slide 31
Blink
Blink and beeps

## Slide 32: QTY 50 is off to the races!
Fuck a tariff
3/17/2026

## Slide 33: ICE Pinout

## Slide 34: Sleep Studies
OG Code vs Sleeps

## Slide 35: OG CODE:
OG CODE:
#define F_CPU 1000000UL
#include <avr/io.h>
#include <util/delay.h>
// Toggle PB2 by writing 1 to PINB bit
static inline void pb2_toggle(void) {
asm volatile("sbi %0, %1" :: "I"(_SFR_IO_ADDR(PINB)), "I"(PB2));
}
// 125 µs half period @ 1 MHz
static inline void half_period_125us(void) {
uint8_t n = 41; // 3*n - 1 = 122 cycles
asm volatile(
"1: dec %[n] \n\t"
"brne 1b \n\t"
"nop \n\t"
: [n] "+r"(n)
);
}
// 4 kHz tone on PB2
static inline void tone_pb2_4khz_ms(uint16_t duration_ms)
{
uint16_t periods = duration_ms * 4;
while (periods--) {
pb2_toggle();
half_period_125us();
pb2_toggle();
half_period_125us();
}
PORTB &= ~(1 << PB2); // force low
}
// 20 ms pulse on PB0
static inline void pulse_pb0_20ms(void)
{
PORTB |= (1 << PB0);
_delay_ms(20);
PORTB &= ~(1 << PB0);
}
int main(void)
{
// PB2 + PB0 outputs
DDRB |= (1 << PB2) | (1 << PB0);
PORTB &= ~((1 << PB2) | (1 << PB0));
tone_pb2_4khz_ms(50);
_delay_ms(50);
tone_pb2_4khz_ms(50);
_delay_ms(50);
tone_pb2_4khz_ms(50);
_delay_ms(50);
tone_pb2_4khz_ms(50);
uint8_t flash_count = 0;
while (1)
{
pulse_pb0_20ms(); // LED pulse every second
flash_count++;
if (flash_count >= 4) // every 4 seconds
{
flash_count = 0;
tone_pb2_4khz_ms(50);
_delay_ms(50);
tone_pb2_4khz_ms(50);
}
_delay_ms(980); // completes ~1 second total (20ms + 980ms)
}
}
1.05mA AVG!

## Slide 36: ChatGPT “Sleeper Code”
600uA Sleep
734uA Average
Better!
The issue:
  I am drawing 600uA sleeping…that’s bad sleep…except it’s really bad hardware

## Slide 37: On-State Power Draws!
300uA
~300uA

## Slide 38: Fixes…
100k
REMOVE*
100k
*DNP This part, it is redundant when you factor in leakage and capacitance of D5

## Slide 39: New Theoretical Sleep Draw
60uA
8 days80days
Not a deal-killer for beta-test, but def. a miss on my part

## Slide 40: Update: 3/20/2026
Replaced resistors R7/R4 with 100ks
Removed R3
New average draw: 180uA!
Sleep Current: 60uA
Sensitivity….questionable it should go up though.
"C:\Users\robot\OneDrive\Documents\Projects\MouseMinder\PowerProfilerData\ATTINY10Sleep_optimized_resistors.csv“
I won’t do this rework to 50x boards…but I’ll rework 1-2 for internal testing.

## Slide 41: Plot

## Slide 42: Dumb idea…3/21/2026
The attiny has stupid low sleep current like 500nA…
  On-par with CR2032 self-discharge…
Why not just wire the piezo direct* into INT0 and use the internal clamping diodes handle the rest? Part count goes WAY down…
*Still want R6 here to limit diode current…

## Slide 43: Circuit Mods…on PCBs I already have…

## Slide 44: Programming Changes
PB2 needs pull-up turned on for sleep mode between pulses.
PB2 is also the interrupt from deep sleep.
PB2 is really the star of the show here.
PB2 is love, PB2 is life.
https://chatgpt.com/share/69bf128c-7c8c-8001-9b17-0a67c42d7913

## Slide 45: It works! Wow. Here’s my schematic

## Slide 46: Improvements and to-dos
SW1 “Test” needs a 10k current limiting resistor, same with SW4 (from 1k).
Still need to probe interrupt line to check for major voltage violations. 20 ohms may not be enough.
Don’t want additional disturbances to disable sensor. Would probably want to move disable function to an unused pin like reset (no additional code!).
100k pulldown arbitrary.
Remove decoupling caps and see what happens.
Keep pads for R&C sensitivity adjustment.

## Slide 47: Update to last slide:
Runs fine with no decoupling caps.
Reset switch to reset pin works a treat.
80uA  4uA deep sleep once I cleaned off my filthy flux.
  6.3 years of idle (ideally)
  Self-discharge of a CR2032 gets us to like 2-5 years.
  Chef’s Kiss.
Let’s measure voltage on PB2 when a trap goes off next.

## Slide 48: Let’s work on a programming Jig for V4
Insert PCB
Press the Test button to begin programming/QC sequence
Program at 5V
Shutdown (don’t want to burn out LED)
Apply 3V to 3V Rail
Tap Piezo and measure analog voltage on PZ+
  Hopefully this triggers the unit
If the unit doesn’t trigger, we can apply power to the Latched_Power Rail
Read Phototransistor on LED
Read Analog Voltage on NGate
Press Reset Button
Test Pass

## Slide 49: Visual Sequence
Insert PCB into Jig
Press “Test” Button to Start
Apply 5V on Battery Pin
Program Success?
LED = RED
ERROR MSG
Disable 5V Power, Apply 3V
Solenoid Tap Power On?
LED = RED
ERROR MSG
LED Blinking?
LED = RED
ERROR MSG
Press “RST” Button
NGATE Goes Low?
LED = RED
ERROR MSG
TEST PASS

## Slide 50: QTY 50 ARRIVED 4/2/2025
They work!
783uA average (3v)!

## Slide 51: POGO Pinout
RST
3R
LC
PD
GN
Top View
Batt
CLK
GND
Latched
DATA
PZ
NGATE
CLK
GND
Latched